## Slide 1
DUST INTELLIGENCE FOR SAUDI SOLAR
SolarGuard
You can't see the dust. We can.
12 OPEN FEEDS
5 MODELS TRAINED
1 VERDICT
Team space-Marines · Riyadh and Dammam
Notes: Open cold. One sentence: SolarGuard tells a Saudi solar plant, every morning, whether cleaning the panels today is worth the money.

## Slide 2
WHAT IT IS
Satellite in. One decision out.
Watch
12 live open feeds: satellite dust, aerosol, wind, sun, rain.
12 FEEDS
Predict
Our own AI models, trained in-house on 4 years of Saudi data.
5 MODELS
Decide
CLEAN or WAIT, priced in riyals. Nothing installed on site.
1 VERDICT
Notes: Three verbs only. The detail comes later.

## Slide 3
HOW IT WORKS
Five steps, satellite to decision
1
Live data
2
AI models
3
Forecasts
4
Economics
5
CLEAN or WAIT
The AI predicts. The physics engine decides.
Notes: Stress step 5: the output is a decision, not a chart.

## Slide 4
PROBLEM
Dust costs more than the cleaning it forces
Evidence
Dust and sandstorms take 20-40% of output: 30-35% measured on the Saudi east coast, 20% from a single sandstorm.
KAUST 2023 · Energies 2022
Today
Operators clean on a fixed calendar, or once a sensor says dust is already high. Neither asks what tomorrow brings.
IEA-PVPS 2022
Severity
At a 100 MWp plant: 10.78M SAR a year cleaning weekly, 16.13M never cleaning at all.
our simulation
Notes: Sources are on the slide. If challenged on 10.78/16.13, say it is our own simulation and give the assumptions: 100 MWp, Dammam, 1,800 SAR per MWp per pass.

## Slide 5
WHAT'S DIFFERENT
From a calendar to an economic forecast
Compared
The closest approaches: a fixed calendar, and dust-threshold sensors that need hardware and react once the loss has started.
closest available
Ours
We turn cleaning into a forecast plus economics: one riyal decision per site per day, with no hardware on site.
our contribution
Trade-off
Output error 0.234 against 2.572 kWh/kWp for the naive guess, 11x better. At a site we have never seen, accuracy drops to AUC 0.785.
tested, limitation stated
Notes: Naming the trade-off openly is deliberate. If asked about sensors, say they measure soiling we already predict from orbit, at a fraction of the cost.

## Slide 6
WHAT IT DELIVERS
One verdict an operator can act on
The target
Beat the 10-day habit on annual cost, at equal or better energy: 6.71M against 8.41M SAR a year, with 18 cleans.
measurable target
Safeguards
A dead feed degrades a single number. If the AI is unavailable the physics engine answers. A bad request returns a clear error.
by design
Boundary
Built for dust-dominated, low-rain desert sites. Snow, hydro and coastal fog are out of scope.
stated, not implied
Notes: The success criterion is on the slide. Both agents of failure are handled in code and covered by tests.

## Slide 7
CAN IT BE BUILT
A 90-day pilot, software only
Assumption
The core number, soiling at 0.2-0.8% per day in Saudi Arabia, comes from published measurement rather than guesswork.
IEA-PVPS 2022 · KAUST 2020
Plan
Pilot at one 100 MWp plant in about 90 days. Estimate: one engineer plus cloud, roughly 15k SAR a month.
estimate, assumptions stated
Risks
Two that matter: no inverter ground truth, and feed outages. Fixes: score against the plant's own inverters, and cache with a physics fallback.
each with a fix
Notes: Say plainly that 15k SAR is our estimate, not a quote, and that cost is dominated by people rather than infrastructure.

## Slide 8
WHAT WE TESTED
Working, and measured against baselines
End to end
Live: pick a site on the map, read the AI prediction, the verdict, and an agent answer with the tools it used.
live, not mocked
Baselines
On 2,244 days it had never seen: storm AUC 0.952, output within 7.7%, soiling within 8.4%.
measured
Failure
We hid a whole site and scored it (AUC 0.785), and we test that the data served can never drift from the data trained on.
reliability reported
Notes: If judges want the failure test, the hidden-site block is in models/ai/metrics.json.

## Slide 9
WHY SAUDI ARABIA
Built here, for here
Local
Trained on 12 Saudi sites, from NEOM to Dammam, on Saudi dust measurements.
local evidence
Benefit
Per 100 MWp site: about 1.7M SAR and 4.5M litres of water saved a year against the 10-day habit.
simulated, assumptions stated
Adoption
The plant's operations manager opens the dashboard each morning, reads CLEAN or WAIT, and sends crews only when it pays.
fits the workflow
Notes: The water figure matters because every pass skipped is water not used in a desert.

## Slide 10
WHAT IS REAL
Built, estimated, and next
Built and tested
Live on 12 open feeds. AI scored on 2,244 unseen days and on a hidden site. The agent cites its sources.
WORKING
Estimated
Output comes from measured weather and physics, not inverter meters. Savings come from a one-year simulation.
MODELLED
Next
Pilot at a real Saudi plant, compared against real inverter output, with site sensors and real costs.
NEXT
Notes: This slide exists to draw the line between what we built and what we estimate. Volunteer it before anyone asks.

## Slide 11
EXTRA · HOW WE TRAINED THE AI
Four years of Saudi dust, then five steps
1
Collect
2
Build 37 inputs
3
Define targets
4
Split honestly
5
Train and blend
18,348 site-days · 12 sites · 37 inputs · 1,540 trees · 22,725 weights
Every input is measured: satellite dust, aerosol, wind, sun and rain, plus how long since it rained.
Every target is defined in code and documented: a measured storm threshold, and two physics formulas fed with measured weather.
Two model families trained for each target and blended by measured skill. No GPU, no ML library: written in numpy, 16 minutes on CPU.
Notes: The honest sentence here: no inverter data is public for Saudi plants, so two of the three targets are documented formulas rather than meter readings.

## Slide 12
EXTRA · WHAT THE MODELS PREDICT
Five models, and how wrong they are
0.952
storm AUC, day +1
7.7%
output error
8.4%
soiling error
· Storm risk at +1, +2 and +3 days, so a crew can be booked before the dust lands.
· Tomorrow's output in kWh and kWh per kWp, which is the number that turns dust into riyals.
· Tomorrow's soiling loss, which drives the clean-or-wait verdict and the water saving.
Notes: Leave-one-site-out: storm AUC 0.785 on a site the models never saw. Say that before being asked.

## Slide 13
EXTRA · THE AGENTIC AI
It asks, waits, then answers
1
Operator asks
2
Model calls tools
3
Server runs them
4
Answer with sources
10 tools over the live data, and retrieval over 672 indexed chunks of soiling research so answers carry citations.
The model never speaks from memory: it asks for data, waits for the real output, then writes the answer.
It acts on the page as well: it moves the map to a site and switches the satellite layer.
Notes: Live answer to quote: 'WAIT, about 12,030 SAR lost this week against 180,000 SAR for one pass, so cleaning now costs roughly 15 times what it recovers.'

## Slide 14
CLEAN or WAIT
From a fixed schedule to a data-driven economic decision.
github.com/Hermes-mahers-bot/solarguard-space
Notes: Stop talking. Let it land, then take questions.